## Slide 1: Project 1：CT Image Reconstruction
Optimization Theory and Algorithm
Fall 2026

## Slide 2: Background
CT: Computer Tomography
  A medical imaging technique used to obtain detailed internal images of the body
Computed tomography of human brain
Modern CT scanner

## Slide 3: Motivation
CT Reconstruction
  A classical inverse problem (projection data to image)
  Basically, CT image is reconstructed by solving a linear system
Multi-angle scanning
Projection data
*(This is Radon transform)
Angle
Scan line
Scan line
Angle

## Slide 4: Problem Formulation
Projection data to image
Projection data
Image
HOW ？

## Slide 5: Problem Formulation
The linear system:
Ax = b
A
x
=
b
.
Na
Nl
Na × Nl
Column-wise
Vectorization
Nx
Ny
Nx × Ny
Column-wise
Vectorization
Unknown
Nx × Ny
Na × Nl

## Slide 6: Problem Formulation
The linear system:
Row-wise view:
Ax = b
aTx = b
aT: the i+(j-1)Nl-th row of A
b: the i+(j-1)Nl-th element of b
i = [1, …, Nl] is the i-th scan line
j = [1, …, Na] is the j-th projection angle

## Slide 7: Problem Formulation
In the current problem:
Ax = b is an overdetermined linear system
(Na × Nl ) > (Nx × Ny)

## Slide 8: Methods: LS Reconstruction
1. Least-square Reconstruction
Ax = b
x = (ATA)-1ATb
Q: b is contaminated by noise in real world.
  Electrical noise, thermal noise, eta.

## Slide 9: Methods: LS Reconstruction
Algorithm
Algorithm: LS reconstruction
Input: A and b x = (ATA)-1ATb Return: x

## Slide 10: Methods: ART Reconstruction
Basic model of Algebraic Reconstruction Technique:
Ax = b
aTi,j projects x into the i-th scan line of j-th angle
The projection data is bi,j
aTx = b
<=> Projecting x into a hyperplane

## Slide 11: Methods: ART Reconstruction
Interpretation
aTx = b
<=> Projecting x into a hyperplane
Projection point b* =
Ax = b
<=> Projecting x into Na × Nl hyperplanes

## Slide 12: Methods: ART Reconstruction
Geometric interpretation
Ax = b
aT1x = b1
aT2x = b2
…
Alternating and iterative projections.

## Slide 13: Methods: ART Reconstruction
Algorithm
Algorithm: ART reconstruction
Input: A and b Initialization: b = 0 (optional) for k = 1 to K for i = 1 to Na × Nl xi+1(k) = projection xi(k) into the hyperplane: aiTx = bi; x(x<0) = 0; end until convergence. end Return: x

## Slide 14: Task
Dataset #1
  Shepp Logan 64
  Na = 90 (from 0° to 179° at a constant step of 2°)
  Nl = round(sqrt(2)*Nx)
  Nx = Ny = 64
Shepp Logan 64

## Slide 15: Task
Dataset #2
  XCAT 128
  Na = 90 (from 0° to 179° at a constant step of 2°)
  Nl = round(sqrt(2)*Nx)
  Nx = Ny = 128
XCAT 128
(Human chest)

## Slide 16: Regular Task (80%)
What you have
  Two datasets, i.e., ground truths
  The corresponding A and noised b (15 dB, 20 dB, 25 dB, 30 dB)
What you need to do
  Reconstructing x via LS .
  Reconstructing x via ART.
  Adding regularizations (L2, L1, TV…) to your reconstructions.
  Analyzing your results.

## Slide 17: Extension (20%)
An underestimated Ax = b system by reducing No. angles
  Low-dose CT, which is helpful to reduce X-ray radiation.
Other solutions
  AI-assisted reconstruction?
  AI-assisted denoising?

## Slide 18
Q & A